Material Safety Data Sheet

Identity : (As Used on Label and List) Product name: 15mm “Tru Flare” Signal Cartridge with audible effect; Trade Name: 15 mm Bearbanger UN Name: Cartridges, signal; UN No.: UN0312; UN Classification Code: 1.4G Date: 04.20.2017

Section I : Manufacturer

“Ballista” Ltd.

Section II – Hazardous ingredients /Identity information

Hazardous components - contain pyrotechnical composition – a mixture of oxidizer and fuel that will rapidly burn when ignited.

OSHA /PEL/ OTHER LIMITS %

Basic Materials: Black Powder No data No data Explosive. Dust may be irritant. Potassium Perchlorate - 10mg/m3 Oral Rat: LD50: 2100mg/kg CAS# 7778-74-7 Powerful oxidizer, highly irritating to skin, eyes and mucous membranes. Violent reaction with (Aluminum & Magnesium), charcoal, sulfur. Absorption can cause methemoglobinemia and kidney injury. Magnesium powder - 15mg/m3 Oral Dog: LD50: 230mg/kg CAS# 7439-95-4 Heart beat alteration. Though rated as an ingestible poison, most serious hazard is from burns. Polyvinyl Chloride, PVC - 1ppm N/A CAS# 9002-86-2 Hazards, if any, would be associated with non-reacted Vinyl Chloride Monomer

Section III – Physical/Chemical Characteristics

Physical state – solid Appearance and Odour : A plastic container having aluminium or paper core insert filled with pyrotechnical mixture. Odourless. Boiling point: N/A Specific Gravity,(H20=1): N/A Melting point: N/A Evaporation Rate: N/A Solubility in Water: N/A

Section IV – Fire and Explosion Hazard Data

Flash Point: Pyrotechnical composition, Self Ignition Point approximately 180 C (350 F) Extinguishing Media: Flood with water, if small number of spilled pieces is involved. Do not use suffocation methods, composition provide its own oxygen. Special Fire Fighting Procedures: Cartridges initiate quickly and contain their own oxygen. Clear the surrounding area and get away. Avoid fire extinguishing, if at least one shipping carton is involved. Use NIOSH/MSHA approved self-contained breathing apparatus when cartridges are involved in fire. Unusual Fire and Explosion Hazards: Each item projects a flaming ball. Contact with strong acids or bases may cause fire or explosion.

Section V - Reactivity Data

Stability: Stable under normal conditions of handling and storage. Incompatibility (Materials to Avoid): Long exposure to water may cause deterioration. Devices should not get in any contact with strong acids and alkali bases. Conditions to Avoid : Heat and Open Flame, Other Sources of Ignition. Hazardous Decomposition Products( Byproducts): Smoke, oxides of nitrogen, sulfur, magnesium, hydrogen monoxide. Hazardous Polymerization : Will not occur.

Section VI – Health Hazard Data

Threshold Limit Value: None Established Route(s) of entry : Inhalation Skin Ingestion Combustion gases, if ignited only No No Health Hazards (Acute and Chronic): Exposure to finished product does not pose any health hazard. Thermal burn hazard from accidental ignition is more significant. Carcinogenicity : Non Signs and Symptoms of Exposure : Prolonged exposure to smoke, generated during shooting of cartridges, may cause irritation of eyes, mucous membranes and respiratory problems. Medical Conditions Generally Aggravated by Exposure: Persons with pre-existing respiratory problems should avoid inhalation of smoke. Inhalation of combustion gases may result in an asthma syndrome. Emergency and First Aid Procedures: Move to fresh air. Call MD if necessary.

Section VI – Precautions for Safe Handling and Storage

Steps to be Taken in Case Material is Released or Spilled: No smoking, open flames or sparking in vicinity of broken or spilled items. Sweep up carefully spilled items into cardboard container. Do not use vacuum cleaner. Waste Disposal Method: Dispose by burning in compliance with Local Regulations and Laws. Precautions to Be Taken in Handling and Storing: Avoid near sources of high temperature, smoking or open flames. Avoid contact with strong acids and alkali bases. Keep shipping cartons cool and dry. Store in dry area, below 71 C (160 F). Other Precautions: No chemical components are released during normal handling and storage. No health hazards are observed during normal handling.

Section VIII – Control Measures

Respiratory Protection: None required Ventilation: Local Exhaust: N/A Mechanical (General): N/A Special: N/A Protective Gloves: Non Required Eye Protection: Non Required Other Protective Clothing and Equipment: N/A Work/Hygienic Practices: No smoking in vicinity of items. Avoid exposure to open flame.

Section IX  -  Shipping Data

UN0312 ,UN Name: Cartridges, signal, Class: 1.4G;    Compatibility group: G;

Packing group: II;    Packing instructions: 135;         Label: 1.4G;

Information supplied by:  Dipl. eng. Ganco Ganev

Expert in Pyrotechnics                /signature/